## Slide 1
Soft SKU
SKU stands for Stock Keeping Unit. Every chipset manufactured has hardware and software features (or in layman's terms functions) available with it. Chipset are mounted on the ECU’s which in turn are installed in the vehicles. These ECU’s can be controlled and managed remotely via commands or operations.
Features of the chipset can be categorized as
Static SKU – Having configuration assigned to the chipset after mass manufacturing. These configurations cannot be changed. Example – Configure number of cores allowed to be used for the Infotainment Unit.
Dynamic SKU – aka Soft SKU. Controlling the configuration of the chipset as and when required. As part of the controlling / monitoring, an operator can decide to control a device feature & behavior of the underlying chipset.
Configuring can be to
    Enable / disable a hardware on the chipset
    Configure the hardware properties / parameters.
    Enable / disable pre-existing software application (a firmware application) running on the chipset
    Configure the pre-existing software application (a firmware application)

## Slide 2
How it Works
Soft SKU enable the device to configure the features dynamically . For example when the user need to switch car type from normal variant to luxury type, it will pull right type of SKU/License and changes profile of car. It will enable the features corresponding to that SKU
Steps of how the SKU works:
Config tool is responsible for creating the SKUs.
The SKUs will be created by defined guidelines that resides inside Config tool. After this step the SKU need to be mapped to corresponding OEM. An OEM will be defined and a program will be created for that OEM for e.g for ECU type or vehicle. Program will be associated with program version, chipsets and a program name.
For each program version, service package for each chipset will be defined .
Per chipset service package, the SKUs and the values of the features will be defined. As part of device onboarding, these SKUs will be applicable to C2C Platform for SKU updates and there will be a default SKU defined .
A default SKU will be associated with program or platform license file for which chipset specific license will be generated from Qualcomm System so that the configurations specified in license file will be enabled and user can experience those features. Features will be updated in alacarte fashion from other user portals.
To enable the Soft SKU on the chipset, the chipsets linked with device need to be identified first. This is done through the attestation process in which the device will send back the chipsets and identifiers associated with it to Qualcomm System.
VEHICLE
IVI
Feature
Secured Storage
Software Apps
License
Chipset1
Feature
Secured Storage
Software Apps
License
Chipset1
Feature
Secured Storage
Software Apps
License
Chipset2
TCU
QWES validate the chipset details. For validating the chipset identity , the chipsets should be on boarded and stored in the backend. For each chipset identified, a license will be published for experiencing its corresponding features. The license will be generated by Qualcomm system (QWES)and send back to the device .There after the features inside chipset get updated with license specific configurations.

## Slide 3
Key Terminologies
SKU – Stock keeping Unit. It is set of features
QWES – Qualcomm portal to generate chipset and platform license file
SMP – Service Management portal
LMS - License Management System
Chipset – Smallest electronic unit of device
Feature – The attribute of chipset
SP – Service Package
OEM – Original Equipment Manufacturer(For e.g Ford, GM etc)
Program – Program for a device or vehicle will be defined for an OEM
Config Tool - Responsible for creating SKUs & associating program with OEM

## Slide 4
As part of device provisioning, chipset onboarding message send to C2C platform
Chipsets need to be identified and validated . For this C2C Platform request QWES to generate nonce and QWES send the nonce to C2C Platform
C2C platform send nonce generated by QWES to device for retrieving the chipset details. Device send back the list of chipset identifiers and SKU id to QWES in encrypted way.
QWES decrypt the chipset identifiers, SKU id, validate the chipset details and send to C2C platform
C2C Platform store the chipset identifiers, SKU id in data store
C2C platform initiate license call for the corresponding SKU id retrieved from device to Qualcomm system(QWES). QWES generate the license and send back to device
The chipset specific license get installed in device and send back response to C2C platform
C2C Platform store the license details and license installation status in data store
Chipset Onboarding/License Installation
C2C Platform
Qualcomm System(QWES)
Chipset Onboarding Message
Get Nonce
Encrypted Chipset Identifiers & SKU Id
Decrypt & Validate Chipset Identifiers, SKU Id
Store Chipset Identifiers & SKU Id
1
2
3
4
5
License Generation
6
Install License
7
8
Data Store
Store License details, status

## Slide 5
OEM
Program
SP for Chipset
SKU2
Features
Program SKU ID
Program Version
Chipsets
Program Name
Features Configuration
SKU1
Hierarchy of OEM Program
Hierarchy of Data
Vehicle
Devices
Configuration Values & States
Configuration Values & States
Chipsets
Properties
Features
License
Configuration Values
Other Firmware applications and configurations

## Slide 6: Example
 | 100 | TCU Manufacturing |  | 
 |  | Platform license | Program SKU id | Sku id
Scenario 1 | All 100 | Lic_1111 | SKU 1111 | 
Scenario 2 | 20 | Lic_1111 | SKU 1111 | 
 | 20 | Lic_2222 | SKU 2222 | 
 | 60 | Lic_4444 | SKU 4444 | 
Chipset Type | Chip1 |  |  |  | 
Features | SKU 1115 | SKU 1114 | SKU 1113 | SKU 1112 | SKU 1111
CPU Core | 16 Core | 16 Core | 8 Core | 4 Core | 2 Core
CPU Frequency | Config 5 feature 2 | Config 4 feature 2 | Config 3 feature 2 | Config 2 feature 2 | Config 1 feature 2
Memory | 16 GB | 16 GB | 8 GB | 8 GB | 4 GB
GPU | Config 5 feature 4 | Config 4 feature 4 | Config 3 feature 4 | Config 2 feature 4 | Config 1 feature 4
Displays | Config 5 feature 5 | Config 4 feature 5 | Config 3 feature 5 | Config 2 feature 5 | Config 1 feature 5
Feature 6 | Config 5 feature 6 | Config 4 feature 6 | Config 3 feature 6 | Config 2 feature 6 | Config 1 feature 6
Feature 7 | Config 5 feature 7 | Config 4 feature 7 | Config 3 feature 7 | Config 2 feature 7 | Config 1 feature 7
Feature 8 | Config 5 feature 8 | Config 4 feature 8 | Config 3 feature 8 | Config 2 feature 8 | Config 1 feature 8
Feature 9 | Config 5 feature 9 | Config 4 feature 9 | Config 3 feature 9 | Config 2 feature 9 | Config 1 feature 9
Feature 10 | Config 5 feature 10 | Config 4 feature 10 | Config 3 feature 10 | Config 2 feature 10 | Config 1 feature 10
Feature 11 | Config 5 feature 11 | Config 4 feature 11 | Config 3 feature 11 | Config 2 feature 11 | Config 1 feature 11
Feature 12 | Config 5 feature 12 | Config 4 feature 12 | Config 3 feature 12 | Config 2 feature 12 | Config 1 feature 12
Feature 13 | Config 5 feature 13 | Config 4 feature 13 | Config 3 feature 13 | Config 2 feature 13 | Config 1 feature 13
Feature 14 | Config 5 feature 14 | Config 4 feature 14 | Config 3 feature 14 | Config 2 feature 14 | Config 1 feature 14